## Slide 1: SMART INDIA HACKATHON 2026
DEPTHWIZARD
One satellite image in, a measurable 3D surface out.
PROBLEM STATEMENT ID
SIH26175
PROBLEM STATEMENT TITLE
DepthWizard - Single-View Height Estimation and 3D Flythrough
THEME
Disaster Management
PS CATEGORY
Software
TEAM ID
47
TEAM NAME (ON PORTAL)
Dev Up
BUILT AND MEASURED, NOT PROPOSED
3.67 m
per-building RMSE against airborne LiDAR
38 %
better than the 5.9 m GlobalBuildingAtlas bar
509 ms
per tile on CPU alone, no GPU in the loop
The palette is the model's own output scale: 0 m at the left, 155 m at the right.

## Slide 2
Dev Up
DEPTHWIZARD
One satellite image in, a measurable 3D surface out. Every submission promises accuracy. This one reports it.
THE PROBLEM
OUR SOLUTION
01
Archives with no height
Decades of Cartosat single-view imagery exist. Stereo and LiDAR cannot be flown into the past.
02
Answers with no confidence
Single-view height is ill-posed. One number implies a certainty the model does not have.
03
Checkpoints are not products
The literature ships weights and an eval script. An analyst needs a scene they can open and check.
One image to a metric DSM
Depth Anything V2 fine-tuned on DFC2019 + GAMUS LiDAR. GeoTIFF out, metadata or not.
Confidence, not just height
A per-pixel sigma beside every height. Where it says unsure, it is wrong — monotonically.
A navigable 3D scene
three.js flythrough, drag-to-compare against reference, and a live error map.
Validation inside the product
RMSE, MAE and correlation against LiDAR — per terrain class, not one flattering average.
Absolute heights, two ways
Copernicus GLO-30, or ground control points via a power-law fit.
Deployable, not demo-ware
No GPU: 536 ms per tile. The viewer is one 15 MB HTML file that opens from disk.
THE PRODUCT, RUNNING — CAPTURES OF THE LIVE VIEWER, NOT MOCK-UPS
SIKKIM, INDIA
967 m of relief across 2 km, image draped on the surface.
OMAHA, HEIGHT ABOVE GROUND
Flat roofs, tree crowns and kerbs resolved at 0.3 m.
OMAHA, MODEL CONFIDENCE
Per-pixel sigma: where the estimate is weak, it says so.

## Slide 3: TECHNICAL APPROACH
Dev Up
ARCHITECTURE — ONE IMAGE TO A CHECKED SURFACE
INPUT LAYER
GeoTIFF with geo metadata
Plain PNG / JPG, no metadata
Cartosat single-view archive
NORMALISATION
Ground sample distance read from metadata
Auto-zoom and resample to a 0.3 m scale
MODEL CORE — DEPTH ANYTHING V2
ViT encoder
DPT neck
Fine-tuned on DFC2019 + GAMUS
DUAL HEAD
Height mu, per pixel
Log-variance sigma, per pixel
POST-PROCESS
518 px tiling, overlap blend, TTA
Scale anchor: GLO-30 or ground control
OUTPUT LAYER
GeoTIFF DSM
Sigma map
three.js scene, live error map
DEPLOYMENT AND ADOPTION PATH
1
Pilot on what is already open
Run over Bhoonidhi CartoDEM and LISS-4 tiles we can access today, and publish per-terrain metrics rather than one average.
2
Validate on Indian truth
With SAC-held Cartosat stereo or DGPS control points, the Sikkim model-vs-model check becomes a real accuracy number.
3
Integrate
Ships as a container behind an internal API. The viewer needs no server and opens from disk on an analyst's own machine.
4
Scale across the archive
Batch the back catalogue. Every new acquisition gains a height layer at no extra tasking cost.
DECISIONS, AND WHY
The head was chosen by measurement
Regression, binned and head-tail-cut heads were all scored. All three land at a 0.43–0.49 slope, so the simplest ships.
Uncertainty is calibrated
ECE 0.063, sigma-vs-error rank correlation +0.866 on held-out tiles.
Export is checked, not assumed
ONNX agrees with PyTorch to 0.0007 cm over 804,972 inputs; int8 costs 0.030 m.
Resolution is handled explicitly
Auto-zoom resamples by GSD, recovering all but 3.6% of the coarse-input penalty.
HOW IT IS VALIDATED
Split region-disjoint, not random — adjacent tiles share buildings.
Scored on 80 whole tiles, 11,983,760 pixels, 3,090 buildings.
Reported per urban / sparse / forested / mixed, and per height band.
Held back the test split is untouched until the very end.
TECHNOLOGY STACK — EVERY DEPENDENCY FREE AND OPEN
Python 3.10
PyTorch
Hugging Face
ONNX Runtime
NumPy / SciPy
GDAL / rasterio
three.js
Docker

## Slide 4: FEASIBILITY AND VIABILITY
Dev Up
TECHNICALLY PROVEN
Built and measured, not proposed.
OPERATIONALLY SIMPLE
One image in. No GPU, no network.
ECONOMICALLY VIABLE
Every dependency free and open.
SOCIALLY USEFUL
Planning, disaster and forestry use height.
ACCURACY ACROSS THE FOUR LANDSCAPES ISRO NAMES
Three of four classes sit under 3.4 m, and correlation never drops below +0.58. The fourth is the honest problem, and it is one specific thing.
URBAN 13.86 M, DECOMPOSED
79% of squared error comes from 1.9% of buildings. Under 10 m — 94% of the stock — we are at 1.4 m. Urban RMSE is 60 tall buildings dominating a squared metric.
THE TWO REAL RISKS, AND WHAT ANSWERS THEM
No Indian ground truth exists to validate against
Our only Indian check is Sikkim against Google Open Buildings: bias −6.94 m on 168 footprints. That is model-vs-model agreement, not accuracy, and we report it as such. No public Indian scene carries LiDAR truth.
Tall buildings compress toward the mean
A data problem, not an architecture one: training tops out at 82.8 m while validation reaches 155.3 m. Answered by a power-law control-point fit that cuts tall-tile RMSE 24.9%, and structurally by adding tall-building LiDAR.
WHAT REDUCES THE INDIAN-DOMAIN RISK BEFORE WE HAVE THE DATA
Resolution auto-zoom normalises GSD; measured to recover all but 3.6%.
Look angle off-nadir spans 4.8 to 28.9 degrees in DFC, so degradation is measurable on data we hold.
Terrain leakage ruled out — on 31-degree slopes, height-vs-slope correlation is −0.044.
Licensing every dependency is free and open, so nothing blocks deployment on ISRO imagery.

## Slide 5: IMPACT AND BENEFITS
Dev Up
WHO IT SERVES
ISRO AND SAC
Height from single-view Cartosat archives, no new acquisition.
URBAN PLANNING
Building heights for FSI checks and shadow studies under AMRUT.
DISASTER RESPONSE
Post-event surface models where a stereo pair cannot be waited for.
FORESTRY
Canopy height proxies for biomass and encroachment monitoring.
TELECOM ROLLOUT
Line-of-sight and tower siting without a costly LiDAR survey.
DEPTH WIZARD
KEY BENEFITS
One image replaces a stereo pair — no revisit wait.
No GPU procurement: 36.8 MB runs on a field laptop.
Decades of existing archive gain a new product.
Municipal bodies get heights with no survey budget.
Disaster teams get a surface model in minutes.
Free and open — adoptable by any state agency.
1 image
input needed, not a stereo pair
0 GPUs
536 ms per tile on a laptop CPU
36.8 MB
the whole model, quantised, offline
4 terrains
scored separately, never averaged
Every one of these runs on imagery that has already been flown and already been paid for. The cost avoided is the second acquisition, not the first.

## Slide 6: RESEARCH AND REFERENCES
Dev Up
RESEARCH THAT CHANGED WHAT WE BUILT
Depth Anything V2 Yang et al., NeurIPS 2024. The backbone we fine-tune.
HTC-DC Net Chen et al., TGRS 2023. Head-tail cut, distribution constraints.
Depth Any Canopy Ouaknine et al., 2024. The recipe for aerial height.
Beta-NLL Seitzer et al., ICLR 2022. Keeps the mean head learning.
IM2HEIGHT, TSE-Net Prior single-view height — our baseline for the field.
DATA AND REFERENCE SURFACES
DFC2019 Track 1 US3D at 0.3 m GSD with airborne LiDAR truth.
Copernicus GLO-30 Free 30 m global DEM; the absolute metric anchor.
GlobalBuildingAtlas Published 5.9 m RMSE over Asia — the external bar.
GAMUS ISRO's recommended set. 6,204 tiles, 0.33 m, DC and Philadelphia.
Google Open Buildings A cross-check over India, never used as truth.
TRIED, MEASURED, REJECTED
Ordinal / binned head All heads land at a 0.43–0.49 slope. No gain.
Shadow photogrammetry Oracle shadows reach r 0.503; the net reaches 0.787.
LDS tail reweighting Pixels above 20 m are 7.5% but carry 78.8% of error.
Two-model ensemble Error correlation 0.925 — averaging buys nothing.
Global de-compression A rescale moves error, it does not remove it.
PROBES WE RAN, AND WHAT EACH CLOSED
01 Tall buildings Data, not capacity — and GAMUS then proved it.
03 Guided filtering Squaring off roofs made every metric worse.
04 Where detail went Detail follows the ground area one token covers.
05 Eval resolution Cartosat-class input costs 3.6% after auto-zoom.
06 Height compression Measured: ours = 0.473 × truth + 2.66 m.
HOW WE COMPARE
PARAMETER
STEREO OR LIDAR SURVEY
PUBLISHED SINGLE-VIEW
DEPTHWIZARD
One archived image
Absolute metric height
Per-pixel uncertainty
Scored per terrain
Runs with no GPU
3D viewer shipped
Failure modes published
yes
partial
no
Two rows the alternatives win. A stereo survey gives absolute height directly and ships mature viewers — the table is only useful to a panel if the rows we lose are still in it.
THE BAR WE ARE MEASURED AGAINST
3.464 m per-building RMSE against airborne LiDAR, versus 5.9 m published for Asia. Scored on 3,090 buildings across 80 held-out tiles. Where it fails: buildings above 20 m are under-called by 15.6 m. We pre-registered −13 m and missed it. GAMUS improved it significantly (p = 0.0002); no open data at this resolution reaches 50 m.
PITCH VIDEO QR