## Slide 1: SMART INDIA HACKATHON 2026
DEPTHWIZARD
One satellite image in, a measurable 3D surface out.
PROBLEM STATEMENT ID
SIH26175
PROBLEM STATEMENT TITLE
Single-View Height Estimation and 3D Terrain Visualisation
THEME
Space Technology
PS CATEGORY
Software
TEAM ID
<fill from portal>
TEAM NAME (ON PORTAL)
Dev Up
BUILT AND MEASURED, NOT PROPOSED
3.62 m
per-building RMSE against airborne LiDAR
39 %
better than the 5.9 m GlobalBuildingAtlas bar
509 ms
per tile on CPU alone, no GPU in the loop
The palette is the model's own output scale: 0 m at the left, 155 m at the right.

## Slide 2
Dev Up
DEPTHWIZARD
One satellite image in, a measurable 3D surface out. Every submission promises accuracy. This one reports it.
THE PROBLEM
OUR SOLUTION
01
Archives with no height
Decades of Cartosat single-view imagery exist. Stereo and LiDAR cannot be flown into the past.
02
Answers with no confidence
Single-view height is ill-posed. One number implies a certainty the model does not have.
03
Checkpoints are not products
The literature ships weights and an eval script. An analyst needs a scene they can open and check.
One image to a metric DSM
Depth Anything V2 fine-tuned on DFC2019 LiDAR. GeoTIFF out, metadata or not.
Confidence, not just height
A per-pixel sigma beside every height. Where it says unsure, it is wrong — monotonically.
A navigable 3D scene
three.js flythrough, drag-to-compare against reference, and a live error map.
Validation inside the product
RMSE, MAE and correlation against LiDAR — per terrain class, not one flattering average.
Absolute heights, two ways
Copernicus GLO-30, or ground control points via a power-law fit.
Deployable, not demo-ware
No GPU: 509 ms per tile. The viewer is one 15 MB HTML file that opens from disk.
THE PRODUCT, RUNNING — CAPTURES OF THE LIVE VIEWER, NOT MOCK-UPS
SIKKIM, INDIA
967 m of relief across 2 km, image draped on the surface.
OMAHA, HEIGHT ABOVE GROUND
Flat roofs, tree crowns and kerbs resolved at 0.3 m.
OMAHA, MODEL CONFIDENCE
Per-pixel sigma: where the estimate is weak, it says so.

## Slide 3: TECHNICAL APPROACH
Dev Up
ARCHITECTURE — ONE IMAGE TO A CHECKED SURFACE
1
INPUT
GeoTIFF, or a plain PNG / JPG with no metadata at all
2
GSD NORMALISE
auto-zoom reads ground sample distance, resamples to 0.3 m
3
DA-V2 BACKBONE
ViT encoder and DPT neck, fine-tuned on DFC2019 LiDAR
4
DUAL HEAD
height mu and log-variance sigma, emitted per pixel
5
TILED INFERENCE
518 px sliding window, overlap blending, plus TTA
6
SCALE ANCHOR
Copernicus GLO-30, or ground control by power-law fit
7
OUTPUTS
GeoTIFF DSM, sigma map, three.js scene with a live error map
HOW IT IS VALIDATED
Split region-disjoint, not random — adjacent tiles share buildings.
Scored on 80 whole tiles, 11,983,760 pixels, 3,090 buildings.
Reported per urban / sparse / forested / mixed, and per height band.
Held back the test split is untouched until the very end.
TECH STACK
Python 3.11
PyTorch
Transformers
ONNX Runtime
NumPy / SciPy
OpenCV
GDAL / rasterio
three.js r169
React
Docker
WHAT SHIPS
An elevation module emitting a GeoTIFF DSM and a sigma map, and a viewer that opens it and checks a height against reference data. No GPU, no network.
DECISIONS, AND WHY
The head was chosen by measurement
Regression, binned and head-tail-cut heads were all trained and scored. All three land at a 0.43–0.49 slope, so the simplest ships.
Uncertainty is calibrated, not decorative
ECE 0.077, and a sigma-vs-error rank correlation of +0.829 on held-out tiles.
Export is checked, not assumed
ONNX agrees with PyTorch to 0.0010 cm over 804,972 inputs. int8 costs 0.161 m for a 63% smaller file.
Resolution is handled explicitly
Auto-zoom reads GSD from metadata and resamples, recovering all but 3.6% of the coarse-input penalty.

## Slide 4: FEASIBILITY AND VIABILITY
Dev Up
TECHNICALLY PROVEN
Built and measured, not proposed.
OPERATIONALLY SIMPLE
One image in. No GPU, no network.
ECONOMICALLY VIABLE
Every dependency free and open.
SOCIALLY USEFUL
Planning, disaster and forestry use height.
ACCURACY ACROSS THE FOUR LANDSCAPES ISRO NAMES
Three of four classes sit under 3.4 m, and correlation never drops below +0.58. The fourth is the honest problem, and it is one specific thing.
URBAN 13.86 M, DECOMPOSED
79% of squared error comes from 1.9% of buildings. Under 10 m — 94% of the stock — we are at 1.4 m. Urban RMSE is 60 tall buildings dominating a squared metric.
THE TWO REAL RISKS, AND WHAT ANSWERS THEM
No Indian ground truth exists to validate against
Our only Indian check is Sikkim against Google Open Buildings: bias −6.94 m on 168 footprints. That is model-vs-model agreement, not accuracy, and we report it as such. No public Indian scene carries LiDAR truth.
Tall buildings compress toward the mean
A data problem, not an architecture one: training tops out at 82.8 m while validation reaches 155.3 m. Answered by a power-law control-point fit that cuts tall-tile RMSE 24.9%, and structurally by adding tall-building LiDAR.
WHAT REDUCES THE INDIAN-DOMAIN RISK BEFORE WE HAVE THE DATA
Resolution auto-zoom normalises GSD; measured to recover all but 3.6%.
Look angle off-nadir spans 4.8 to 28.9 degrees in DFC, so degradation is measurable on data we hold.
Terrain leakage ruled out — on 31-degree slopes, height-vs-slope correlation is −0.044.
Licensing every dependency is free and open, so nothing blocks deployment on ISRO imagery.

## Slide 5: IMPACT AND BENEFITS
Dev Up
WHO IT SERVES
ISRO AND SAC
Height from single-view Cartosat archives, no new acquisition.
URBAN PLANNING
Building heights for FSI checks and shadow studies under AMRUT.
DISASTER RESPONSE
Post-event surface models where a stereo pair cannot be waited for.
FORESTRY
Canopy height proxies for biomass and encroachment monitoring.
TELECOM ROLLOUT
Line-of-sight and tower siting without a costly LiDAR survey.
DEPTH WIZARD
KEY BENEFITS
One image replaces a stereo pair — no revisit wait.
No GPU procurement: 36.8 MB runs on a field laptop.
Decades of existing archive gain a new product.
Municipal bodies get heights with no survey budget.
Disaster teams get a surface model in minutes.
Free and open — adoptable by any state agency.
1 image
input needed, not a stereo pair
0 GPUs
509 ms per tile on a laptop CPU
36.8 MB
the whole model, quantised, offline
4 terrains
scored separately, never averaged

## Slide 6: RESEARCH AND REFERENCES
Dev Up
RESEARCH THAT CHANGED WHAT WE BUILT
Depth Anything V2 Yang et al., NeurIPS 2024. The backbone we fine-tune.
HTC-DC Net Chen et al., TGRS 2023. Head-tail cut, distribution constraints.
Depth Any Canopy Ouaknine et al., 2024. The recipe for aerial height.
Beta-NLL Seitzer et al., ICLR 2022. Keeps the mean head learning.
IM2HEIGHT, TSE-Net Prior single-view height — our baseline for the field.
DATA AND REFERENCE SURFACES
DFC2019 Track 1 US3D at 0.3 m GSD with airborne LiDAR truth.
Copernicus GLO-30 Free 30 m global DEM; the absolute metric anchor.
GlobalBuildingAtlas Published 5.9 m RMSE over Asia — the external bar.
ISRO Bhoonidhi Registered. CartoDEM 30 m and LISS-4 are the free tiers.
Google Open Buildings A cross-check over India, never used as truth.
TRIED, MEASURED, REJECTED
Ordinal / binned head All heads land at a 0.43–0.49 slope. No gain.
Shadow photogrammetry Oracle shadows reach r 0.503; the net reaches 0.787.
LDS tail reweighting Pixels above 20 m are 7.5% but carry 78.8% of error.
Two-model ensemble Error correlation 0.925 — averaging buys nothing.
Global de-compression A rescale moves error, it does not remove it.
PROBES WE RAN, AND WHAT EACH CLOSED
01 Tall buildings More tall examples? No — training tops out at 82.8 m.
03 Guided filtering Squaring off roofs made every metric worse.
04 Where detail went Detail follows the ground area one token covers.
05 Eval resolution Cartosat-class input costs 3.6% after auto-zoom.
06 Height compression Measured: ours = 0.473 × truth + 2.66 m.
HOW WE COMPARE
PARAMETER
STEREO OR LIDAR SURVEY
PUBLISHED SINGLE-VIEW
DEPTHWIZARD
One archived image
Absolute metric height
Per-pixel uncertainty
Scored per terrain
Runs with no GPU
3D viewer shipped
Failure modes published
yes
partial
no
TWO ROWS THE ALTERNATIVES WIN
A stereo survey gives absolute height directly and ships mature viewers. The table is only useful to a panel if the rows we lose are still in it.
THE BAR WE ARE MEASURED AGAINST
3.62 m per-building RMSE against airborne LiDAR, versus 5.9 m published for Asia. Scored on 3,090 buildings across 80 held-out tiles.